## Slide 1
US Business 77
Corridor Study
2016 AMPO Annual Conference
Fort Worth, Texas
October 28, 2016

## Slide 2: Outline of Presentation
Business 77 Study Purpose
Corridor Stakeholder Engagement
Development of Concepts
Illustrative Design
Implementation Strategy

## Slide 3: Business 77 Corridor History
1930’s: Original US 77/81 – Dallas to San Antonio Hwy
1950 – Freeway section built from US 84 to Brazos River
  US 84 realigned to Waco Dr
  Plans to convert entire US 77/81 corridor to a freeway
1956: Establishment of Interstate Hwy System
  Decision to locate IH-35 on separate alignment
1960’s to 1980’s
  Closure of Connally AFB, General Tire
  Shift of land uses to IH-35 corridor

## Slide 4: Business 77 Current Status
Traffic Volumes below Capacity
  Elm Mott to US 84 – 30% to 50% of capacity used
  US 84 to Brazos River – 15% to 20% of capacity used
Facility will require reconstruction within next 20 to 25 years
  Patched pavement and joints
  90 to 100 year old bridge structures

## Slide 5: Business 77 Study Purpose
If reconstruction will be necessary, should we:
Rebuild with current design?
If we redesign, do we:
  Create boulevard design?
  Reduce structures & lane-miles for maintenance?
  Improve property access?
  Provide same, less or more capacity for future?

## Slide 6: Project Steering Committee
Agency members: TxDOT, MPO, Waco Transit, Waco, Bellmead, Lacy Lakeview
Stakeholder members: business, residential, organizations
Role:
  Provide input, guidance
  Review and provide feedback
  Encourage local involvement

## Slide 7: Project Scope

## Slide 8: Project Schedule
Project Workshop Feb 1-4
Project Schedule

## Slide 9: Public Workshop Process

## Slide 10: Public Meetings during Workshop
Feb 1 Public Meeting – Issues & Needs
Format: Presentation with Breakout Sessions
Presentation: Purpose, Existing Conditions
Breakout Sessions: Constraints, Issues, Needs, Opportunities
Feb 4 Public Meeting – Concepts and Priorities
Format: Presentation with Breakout Sessions
Presentation: Concepts by Zone, Major Improvement Items
Breakout Sessions: Feedback on Concepts, Priorities

## Slide 11: Table exercises – Corridor Character
What do you like & wish to preserve?
What do you dislike & want to change?
What is missing that you like to see created?
Open to all opportunities

## Slide 12: What We Heard- What you want on the corridor:

## Slide 13: Public Open House during Workshop
Feb 2 & 3 from 4:00 to 6:00 pm
Format: Drop in on the project team working session
Presentation: View the work in progress
Interaction: Ask questions, provide comments

## Slide 14: Key Person Interviews during Workshop
Feb 2 & 3 from 8:00 am to 3:00 pm
Format: Individual and small group discussions
Invitees: Agencies, businesses, land owners, residents
Interaction: Team questions, agency & public input
 | Tuesday Feb 2, 2016 | Wednesday Feb 3, 2016 | Thursday Feb 4, 2016
8am |  |  | 
8:30am |  | Keith Bond, Public Works and City Manager, City of Lacy-Lakeview | Octavio Garza, Public Works Director, City of Waco
9am |  | Dave Morrow, President Waco Bike Club plus two other members | Mark Mason, Manager of Flint Hills Resources, Chemical Plant
9:30am |  |  | Rock McNair, Baylor University
10am | Dewayne Banks, Business Owners, (254) 855-7521 | Clint Peters, Director of Planning, City of Waco | 
10:30am |  | Megan Henderson, Waco Downtown Development Corp | 
11am | Ed Mazanec, Business Owner - Mazanec Construction | Bo Thomas, City Manager, City of Bellmead | 
11:30am | Dale Fisseler, City of Waco, CM; Wiley Stem, Deputy CM; Deidra Emerson, ACM |  | 
12pm |  |  | 
12:30pm |  |  | 
1pm | Pastor Jimmy Hunter, Toliver Chapel Baptist Church |  | 
1:30pm |  |  | 
2pm | Wes Holt, Connally ISD Superintendant, (254) 296-6460 | Solomon Thomas, TxDOT | 
2:30pm | David Marek, Wallace Group (for Developers of MLK east of BUS 77) |  | 

## Slide 15: Character Zones
McLane Stadium
Marlin Hwy Interchange
MLK Jr. Blvd
Baylor University

## Slide 16: Character Zones
SH 6 to
College Station
Connects
SH 6 and IH-35

## Slide 17: Character Zones
IH-35 Interchange
(Redesigned by TxDOT
Railroad
Baylor Research and Innovation Collaborative

## Slide 18: Character Zones
US 84 Interchange

## Slide 19: Character Zones
Retail
HEB
Sam’s Club
Behrens Circle

## Slide 20: Character Zones
FM 3051/Loop 340 Interchange
Walmart
Home Depot

## Slide 21: Character Zones
Tymco
Alamo Steel
Meyers Ln
Railroad

## Slide 22: Character Zones
Flood Plain, Rural
Residential
E. Craven Ave

## Slide 23: Character Zones
E. Crest Dr
Connally ISD
TSTC

## Slide 24: Character Zones
Connally ISD
IH-35 Interchange

## Slide 25
Pedestrians and Bicyclists

## Slide 26: Special Use Parallel Roads
Convert to 1-way
Add parking, as needed
Add pedestrian amenities, as needed
At industrial, convert ownership and maintenance

## Slide 27: Emerging Features
Boulevard
Access control
Special use parallel roads
Bicycle and pedestrian accommodations
Roadway network enhancement
Special intersection treatments

## Slide 28: Boulevard Section
Four 13’ travel lanes w/ curbs
Approximately 20’ median
Retain center drainage
Create pass-thru curbs to median drainage
Landscape/xeriscape some median areas
Remove shoulders and add outside curbs, pass-thru where needed

## Slide 29: Access Control
Left turn bays in median
Formalize driveways
Driveway consolidation if possible
Retain key parallel service roads
Enhance parallel Old Dallas Road
Provide ample strategic median openings
Keep some short segments of parallel roads for special uses
Create shared parking zones
Physical Medians, Openings, Driveways

## Slide 30: Special Intersection Treatments
Bring multi-level intersections back to grade
  Marlin Highway
  Orchard Lane
  Waco Drive (Potts interchange)
Consider modern roundabouts at key locations
  Marlin Highway
  Orchard Lane
  Waco Drive
  Behrens Circle
  Craven Avenue
  Crest Drive

## Slide 31: Modern Roundabouts
Perform as good of better than signals under certain traffic conditions
Create a less intense traffic operation
Can denote transition between character zones

## Slide 32
Traffic Circle
Modern
Roundabout
Mini-Traffic
Circle
Modern
Roundabouts
In Context

## Slide 33
Before:
Traffic Circle
Worcester, MA

## Slide 34
After:
Roundabout
Worcester, MA

## Slide 35: Comparison to the size of Waco’s Old Traffic Circle
Worcester, MA
Waco, TX

## Slide 37: Illustrative Design of BUS 77, p1
BUS 77
Bus Pullover
Sidewalk
Sidewalk
Cadet Way
N. Lacy Drive
N

## Slide 38: Illustrative Design of BUS 77, p2
BUS 77
Bus Pullover
Sidewalk
Sidewalk
Cadet Way
N. Lacy Drive (end)
N. Lacy Drive
N

## Slide 39: Crest Drive (FM 2417)
US BUS 77
CREST
US BUS 77
CREST DRIVE
N
Closely spaced stops on Crest Drive create driver confusion

## Slide 40: Crest Drive (FM 2417)
US BUS 77
CREST
Potential Realignment
CREST DRIVE
N

## Slide 41: Illustrative Design of BUS 77, p3
BUS 77
Sidewalk
Sidewalk
Crest Drive
Central Street
Spring
Flower Ln
N. Lacy Drive
N
Parallel Road for local circulation

## Slide 42: Craven Avenue
US BUS 77
CRAVEN
N
Closely spaced stops on Craven Avenue create driver confusion

## Slide 43: Craven Avenue
US BUS 77
CRAVEN
US BUS 77
N

## Slide 44: Illustrative Design of BUS 77, p4
BUS 77
N. Lacy Drive
Old Dallas Road
Craven Drive
N

## Slide 45: Illustrative Design of BUS 77, p5
BUS 77
N. Lacy Drive
Old Dallas Road
RR Service Track
N

## Slide 46: Lakeshore Gateway
US BUS 77
REMNANT RD
REMNANT RD
LOOP 340
LOOP 340
OLD DALLAS RD
PECAN LN
REVERE RD
Traffic Analysis: Roundabout not good
Traffic Analysis: Signal works well
N
N

## Slide 47: Illustrative Design of BUS 77, p6
Cross-
Over
Lanes
Old Dallas Road
BUS 77
RR Service Track
Myers Lane
Loop 340
N

## Slide 48: Illustrative Design of BUS 77, p7
Shared Parking
BUS 77
Old Dallas Road
Hogan Lane
Hogan Lane
Hogan Lane
Behrens Circle
I-35
N

## Slide 49: Illustrative Design of BUS 77, p8
BUS 77
Behrens Circle
Shared Parking
Shared Parking
Shared Parking
Behrens Circle
Oaklawn Street
N

## Slide 50: Potts Interchange
WACO DR
(US 84)
US BUS 77
US BUS 77
HILLSBORO RD
US BUS 77
Traffic Analysis: Roundabout works well
N

## Slide 51: Potts Interchange Impact on Local Community Vitality
Historical Significance:
Provision of interchange is historic
Design of bridge structure is not
Possible to remove structure if:
  Show not needed or negative
  Show to be better without it
  Show acceptable traffic without it
N

## Slide 52: Illustrative Design of BUS 77, p9
BUS 77 (N. La Salle Avenue)
US 84 (Waco Drive)
Hillsboro Drive
N

## Slide 53: Potts Interchange Impact on Local Community Vitality
N

## Slide 54: Illustrative Design of BUS 77, p10
BUS 77 (N. La Salle Avenue)
I-35 (TxDOT Planned Configuration)
N

## Slide 55: Marlin Hwy & Orchard Lane
US BUS 77
ORCHARD
US BUS 77
UPRR
<- TO I-35
Historical Significance:
Provision of interchange is historic
Design of bridge structure is not
Possible to remove structure if:
  Show not needed or negative
  Show to be better without it
  Show acceptable traffic
Marlin Highway
US BUS 77
N

## Slide 56: Marlin Hwy @ Orchard Lane & BUS 77
Potential Extension
ORCHARD
US BUS 77
US BUS 77
OLD US BUS 77 Local Industrial Road
N
Traffic Analysis: Roundabout works well
N

## Slide 57: Illustrative Design of BUS 77, p11
BUS 77 (N. La Salle Avenue)
Orchard Lane
Kendall Lane
Katy Lane
Cotton Belt Street
Outside Lane ->
Buffered Bike Lane
N

## Slide 58: Illustrative Design of BUS 77, p12
BUS 77 (N. La Salle Avenue)
Industrial Boulevard
Landscape Buffer
Truck Staging
Cherry St.
E. 10th St.
N
Excess
Land

## Slide 59: Illustrative Design of BUS 77, p13
Proposed Multifamily
Excess
Land
Landscape Buffer
Industrial Boulevard
Marlin Highway Spur 484
Martin Luther King Blvd Ext’n
BUS 77 (N. La Salle Avenue)
N
Excess
Land

## Slide 60: Illustrative Design of BUS 77, p14
Proposed Hotel
Proposed Multifamily
Industrial Blvd
Marlin Highway Spur 484
Martin Luther King Blvd Ext’n
BUS 77 (N. La Salle Avenue)
N

## Slide 61: Implementation Priority Strategy
Safety
Functional Improvements
Economic Development

## Slide 62: Priority Set 1: Safety Improvements
BUS 77 @ Crest Drive
  Eliminate service road crossing Crest Drive
  Align Spring Flower Lane into intersection
  Use Roundabout for traffic control
Crest Drive
BUS 77
Spring Flower Ln
Central Street

## Slide 63: Priority Set 1: Safety Improvements
BUS 77 @ Craven Avenue
  Eliminate service road (South and North Lacy Drive) crossing Craven Avenue
  Use Roundabout for traffic control to better incorporate East and West Craven Avenues at the intersection
  Not bring Powers Street into roundabout
BUS 77
Craven Avenue

## Slide 64: Priority Set 2: Functional/ED Improvements
BUS 77 @ Marlin Hwy/MLK Blvd
  Eliminate 3-level interchange
  Connect Marlin Hwy to MLK Blvd
  Create boulevard for industry
  Industrial Blvd also serves as event bypass
  Eliminates circuitous routes for industry
Industrial Boulevard
Marlin Highway Spur 484
Martin Luther King Blvd Ext’n
BUS 77 (N. La Salle Avenue)

## Slide 65: Priority Set 2: Functional/ED Improvements
BUS 77 @ Orchard Lane
  Eliminate Orchard Lane overpass
  Eliminate on-ramps/off-ramps
BUS 77 (N. La Salle Avenue)
Orchard Lane

## Slide 66: Priority Set 2: Functional/ED Improvements
BUS 77 @ I-35 (as proposed)
BUS 77 @ US 84 (continuation)
BUS 77
US 84
Hillsboro Drive
I-35
BUS 77

## Slide 67: Discussions with City Councils Waco * Bellmead * Lacy Lakeview
How do these concepts compare to reality for this area?
Would these improvements help businesses to grow?
How can the concepts be improved?
What other factors need to be considered?
What can/should be done sooner than later?

## Slide 68: Project Development Stages
Corridor Study
Construction
MTP inclusion
ROW/utility relocation
Phased
Priority
Environmental
Design
Schematics
TIP/STIP inclusion
Final Design
PS&E
Illustrative Design
Identify
Partnerships
Programs
Bonds