## Slide 1: New Jersey Pilot Study
Testing Potential MAP-21* System Performance Measures
2014 AMPO Annual Conference
October 24, 2014
Keith Miller Principal Planner Data & Forecasting North Jersey Transportation Planning Authority
*Moving Ahead for Progress in the 21st Century Act

## Slide 2: NJTPA Region
Bergen
Essex
Hudson
Hunterdon
Jersey City
Middlesex
Monmouth
Morris
Newark
Ocean
Passaic
Somerset
Sussex
Union
Warren
13 counties, 2 major cities
6.6 million people
3.7 million jobs
Road Network:
147 million vehicle miles each day
26,000 road miles (177 miles toll)
4,800 bridges
Transit Network:
732,000 trips daily
13% of commuters ride transit
250 bus routes
390 miles commuter rail track, 150 stations

## Slide 3: Overview
Pilot Project Approach
Corridors
Data
System Performance Measures
  Delay
  Reliability
Issues, Next Steps

## Slide 4: Project Approach
Test performance measure methodologies
  MAP-21: Congestion, System Performance of Interstate System & NHS
  Test AASHTO*-recommended measures for delay and reliability
  Use archived operations data
  Two New Jersey corridors (Interstate, arterial)
  Propose/test alternate
    Formulations
    Thresholds
    Aggregation
  Assess results – what the values are telling us
  Note barriers, challenges, assumptions, workarounds
  Collaborate with NJDOT
Develop a summary report
  http://www.njtpa.org/Planning/Performance-Analysis/NJPilotReportDraft.aspx
*American Association of State Highway and Transportation Officials
DRAFT

## Slide 5: Fundamental Concepts
Measures deal with roadways (as opposed to trips)
  Segments of roads – and sum up for the region
  Actual speeds, travel times on particular segments
  Reference or threshold speeds and travel times
  Numbers of vehicles, numbers of people traveling
  Types of vehicles (autos, buses, trucks)
Context may be taken into account
  Place type: urban / suburban / rural / etc.
  Functional class
  Other?

## Slide 6: What is a Threshold?
Standard, reference point, expectation
Delay
  Travel time in excess of threshold = delay
  When does “delay” start?
  What “delay” can we impact/afford to address?
Reliability (or Variability)
  “Unexpected” travel time compared to threshold (e.g., 2 times longer than expected)
  What do travelers expect as a “reliable” travel time?
  Dependent on time of day?
  What can we impact/afford to address?

## Slide 7: Pilot Corridors
Chosen based on regional importance, unique features and familiarity
Interstate; rural/urban; local/express; toll/free
NHS freeway/arterial; limited access/ signals; urban/commercial/semi-rural
  Entire length – 67.8 miles
  Divided into 4 sub-corridors:
    - PA border to I-287 (30.8 miles)
    - I-287 to GSP (22.6 miles)
    - GSP to NJ Tpk (5.4 miles)
    - NJ Tpk to Holland Tunnel (9.0 miles)
  Entire length – 45.3 miles
  Divided into 4 sub-corridors:
    - NJ 138 to GSP (14.3 miles)
    - GSP to US 9 (16.1 miles)
    - US 9 to NJ Tpk (9.5 miles)
    - NJ Tpk to Hoes Lane (5.4 miles)

## Slide 8: Data Gathering & Processing
Archived Travel Times
  I-95 Corridor Coalition Vehicle Probe Project (VPP) Suite
Vehicle/Truck/Bus Volumes
  NJDOT Congestion Management System (CMS)
  NJ TRANSIT General Transit Feed Specification (GTFS)
  NJDOT Weigh-in-motion (WIM)
Vehicle Occupancy (Person Volumes)
  Plan4Safety (Crash database)
  NJ TRANSIT (Bus load factors)
Vehicle Probe Project Suite

## Slide 9: Conflation of Travel Time and Volume Data in GIS
Vehicle Probe Project Suite
DISCONNECT
Positional inaccuracy
Segmented differently
Difference in feature identification
Different feature representation

## Slide 10: Threshold Variations
Free-flow travel time
Maximum throughput
Median travel time(s)
“Acceptable” travel time
Policy implications to each!

## Slide 11: Measurement Unit Variations
Vehicles (vehicle-hours, vehicle-miles)
Persons (person-hours, person-miles)
    Auto, bus passengers
Buses
Trucks

## Slide 12: Performance MeasureS: DELAY
Testing Potential MAP-21 System Performance Measures
 | Delay in 2012
I-78 | 3,830,000 person-hours
NJ 18 | 1,070,000 person-hours
Example Results

## Slide 13: Annual Hours of Delay (AHD)
Compare travel times with threshold
  Delay Time = travel time in excess of threshold
  Delay × Volume (vehicles or persons or trucks or buses)
AASHTO Method
  Calculate delay for "average week” x 52 weeks
Alternate Method: Actual Total Annual Delay
  Data for each day in the year
  “Average week” data underestimates annual delay (average may be below threshold even if individual values are above)

## Slide 14: AHD Results Example: I-78 (TMC-level)
Threshold Dramatically Affects What Counts as “Delay”
  Free-flow
  Maximum throughput (85% of posted speed)
  Others tested:
    Yearly median
    Day/Hour median
    “Acceptable” travel time by place type and time-of-day
78-C
78-C
78-D
78-D
N
N
Free-flow
Max. Throughput

## Slide 15: Results of Threshold Variation
Chart: Annual Person-Hours of Delay per mile (thousands)
| 18 Corridor | 18A | 18B | 18C | 18D | 78 Corridor | 78A | 78B | 78C | 78D
Free-flow | 21800 | 2290 | 190 | 56900 | 73500 | 28200 | 9180 | 8080 | 52900 | 124000
Yearly Median | 16000 | 1050 | 165 | 37200 | 65200 | 21800 | 8990 | 7580 | 33700 | 94100
Max Throughput | 12600 | 18 | 68 | 31400 | 48600 | 19100 | 2450 | 2770 | 36700 | 104000
“Acceptable” Speed | 8950 | 0 | 96 | 21900 | 35300 | 9480 | 6030 | 851 | 3120 | 54400
Day/Hr Median | 3130 | 203 | 138 | 6900 | 13100 | 11300 | 6360 | 6080 | 25300 | 26900
Each threshold option has unique policy implications for “delay”
Threshold | Person-hours of Delay | 
 | 18C | 78D
Free-flow | 1,038,000 | 2,320,000
Maximum Throughput | 607,000 | 2,043,000
dense urban area
rural area

## Slide 16: Performance Measures: RELIABILITY
Testing Potential MAP-21 System Performance Measures
 | Reliability in 2012
I-78 | 1.38
NJ 18 | 1.41
Example Results

## Slide 17: Reliability Index How much do travel times vary from day to day?
Reliability of travel times
How much do travel times vary from day to day?
AASHTO method (RI80): 80th percentile longest travel times compared to a threshold TT
RI80: Multiplier to threshold travel time to ensure on-time arrival four out of five days, if traveling in most congested time of day

## Slide 18: Different Thresholds Yield Different Results and Interpretations
Threshold: Free-flow TT
Threshold: Max Throughput TT
Threshold: Yearly Median TT

## Slide 19: Using Thresholds that Take Into Account Time-of-Day
RI80 = Max 80th percentile TT/ Threshold TT
TTRMax = Max (80th percentile TT/ Threshold TT)
Predictable congestion can be reliable
NJTPA formula looks at the expected travel time at the same time of day as the 80th percentile longest time, to get at most unreliable time of day.
AASHTO Formula (RI80)
AASHTO Formula (RI80)
NJTPA Formula (TTRMax)
NJTPA Formula (TTRMax)

## Slide 20: Issues & Challenges
Complexity of analysis, available tools
  data to measure persons, trucks, buses
  data on arterials (signalized, improved probes)
How to interpret reliability
  worst time of day? predictability? variability?
How to aggregate meaningfully
  weighting to represent the whole system, customers, trips
How to set appropriate thresholds
  consistency, context-sensitive?

## Slide 21: Next Steps
    Continue to coordinate with partners
Explore the policy implications of thresholds
Measuring changes over time, from place to place
Test corridors/years with recently completed projects (“Telling the story” about project effectiveness)
Measure entire trips (O-D data needed)
Emphasize users, land use context, supporting economic growth, efficient use of infrastructure, environment, and other critical planning priorities
MAP-21 proposed rule (January?)
February?

## Slide 22: Thank You
One Newark Center, 17th Floor
Newark, NJ 07102
(973) 639-8400
www.njtpa.org
Keith Miller Principal Planner Data & Forecasting
kmiller@njtpa.org