## Slide 1: Using NPMRDS Data for System Performance
Chris Upchurch
Wichita Area Metropolitan
Planning Organization

## Slide 2: MAP-21 System Performance Measures
Level of Travel Time Reliability
Peak Hour Travel Time Ratio
Truck Travel Time Reliability
Average Truck Speed
Notes: Earlier this year FHWA released a proposed rule for the System Performance measures.
You'll notice the CMAQ measures aren't listed.
The Wichita region is not a non-attainment area, so I haven't really delved into those.

## Slide 3: MAP-21 System Performance Measures
How many of you plan to calculate these yourselves?

## Slide 4: MAP-21 System Performance Measures
How many of you plan to calculate these yourselves?
How many plan to hire a consultant or buy off-the-shelf software?

## Slide 5: MAP-21 System Performance Measures
How many of you plan to calculate these yourselves?
How many plan to hire a consultant or buy off-the-shelf software?
How many haven’t made a decision?
Notes: I'm hoping that what I have to say will be useful to all three groups.

## Slide 6: What is NPMRDS?
National
Performance
Management
Research
Data
Set
Notes: All of these measures rely on the National Performance Management Research Data Set or NPMRDS

## Slide 7: What is NPMRDS?
Travel time data for road segments
  5 minute time increments (epochs)
Covers the National Highway System
Travel time data
  All vehicles
  Trucks

## Slide 8: How many have downloaded NPMRDS data and looked at it?

## Slide 9: How many of you have done something with NPMRDS data?

## Slide 10: Tools for NPMRDS
Notes: This is what it looks like when Excel breaks down and cries.
The file is too big for Excel to open.
For Kansas each month's file is about a gigabyte
Excel will show you the first few thousand rows.

## Slide 11: Tools for NPMRDS
Statistical Tools
Databases
Custom software
Notes: So you need some sort of specialized tool.

## Slide 12: Mismatches between the NHS and NPMRDS
Notes: The first potential pitfall:
NPMRDS claims to be the National Highway System
At least in Wichita, it's not.

## Slide 13: Level of Travel Time Reliability
Divide:
  80th Percentile Speed
  50th Percentile speed
If a segment has a ratio of <1.5 it is considered reliable
Measure: Percentage of reliable mileage

## Slide 14: Level of Travel Time Reliability: Handling Missing Data
For epochs with missing data, use the posted speed limit for that segment
Speed limits often change within a travel segment
Notes: For epochs with no travel time data, use the posted speed limit.
At WAMPO we found we did not have good speed limit data
Google street view
For many segments, the speed limit changes in the middle of the segment
The proposed rule does not specify how to handle this.
Submitted a comment
We've assigned the higher speed limit to the entire NPMRDS segment
Probably not the best way but it is the simplest for testing purposes

## Slide 15: Level of Travel Time Reliability: When to look at
Weekdays:
  6 am to 10 am
  10 am to 4 pm
  4 pm to 8 pm
Weekends:
  6 am to 8 pm
Calculate each time period separately
All four time periods must be reliable for the segment to be considered reliable
Notes: Each time period is calculated separately.
Look at 6-10am every weekday for the entire year.
Look at 10am-4pm every weekday for the entire year.
Look at 4-8pm every weekday for the entire year.
Look at 6am-8pm every weekend for the entire year.
Each of these four time periods must be reliable for a segment to be reliable

## Slide 16: Level of Travel Time Reliability: Geography
Interstates within the MPO boundary
Non-Interstate NHS within the MPO boundary

## Slide 17: Peak Hour Travel Time Ratio
Define a desired travel time for each segment
Divide:
  Desired travel time
  Actual travel time
If a segment has a ratio of <1.5 it is meets expectations
Measure: Percentage of mileage that meets expectations

## Slide 18: Level of Travel Time Reliability: Handling missing data
Ignore epochs with no data

## Slide 19: Level of Travel Time Reliability: Outliers
Remove epochs with travel speeds:
  Below 2 mph
  Over 100 mph

## Slide 20: Peak Hour Travel Time Ratio: When to look at
Weekdays only
Exclude federal holidays
Six 1-hour segments
  6-7am, 7-8am, 8-9am, 4-5pm, 5-6pm, 6-7pm
Calculate the ratio between desired and actual for each hour
Select the hour with the highest average

## Slide 21: Level of Travel Time Reliability: Geography
Only urbanized areas with a population over 1 million
Interstates within the Urbanized Area Boundary
Non-Interstate NHS within the Urbanized Area Boundary
Notes: Only urbanized areas with a population over 1 million
In the proposed rule, FHWA asked for feedback on lowering this threshold

## Slide 22: Truck Travel Time Reliability
Divide:
  95th percentile travel time
  50th percentile travel time
If a segment has a ratio of <1.5 it is considered reliable
Measure: Percentage of reliable mileage

## Slide 23: Truck Travel Time Reliability: Handling missing data
For epochs with missing data:
  Use "all vehicle" travel times if available
  If not, use the posted speed limit for that segment

## Slide 24: Truck Travel Time Reliability: When to look at
24/7/365

## Slide 25: Travel Time Reliability: When to look at
Interstate System within the MPO Boundary

## Slide 26: Average Truck Speed
Calculate the average struck speed over the year
If the average speed is over 50mph the segment is uncongested
Measure: the percentage of the system uncongested

## Slide 27: Average Truck Speed: Handling missing data
For epochs with missing data:
  Use "all vehicle" travel times if available
  If not, use the posted speed limit for that segment

## Slide 28: Average Truck Speed: When to look at
24/7/365

## Slide 29: Average Truck Speed: Geography
Interstate System within the MPO Boundary

## Slide 30: Missing Data
Level of Travel Time Reliability | Use posted speed limits
Peak Hour Travel Time Ratio | Ignore epochs with no data
Truck Travel Time Reliability | Substitute "all vehicles" time Otherwise, use posted speed limit
Average Truck Speed | Substitute "all vehicles" time Otherwise, use posted speed limit

## Slide 31: Outliers
Level of Travel Time Reliability | 
Peak Hour Travel Time Ratio | Remove time periods <2mph or >100mph
Truck Travel Time Reliability | 
Average Truck Speed | 

## Slide 32: When to look at
Level of Travel Time Reliability | 6-10am, 10am-4pm, 4-8pm, Weekends 6am-8pm All must be reliable
Peak Hour Travel Time Ratio | 6-7am, 7-8am, 8-9am, 4-5pm, 5-6pm, 6-7pm Look at the hour with the highest average
Truck Travel Time Reliability | 24/7/365
Average Truck Speed | 24/7/365

## Slide 33: Geography
Level of Travel Time Reliability | Interstates within the MPO boundary Non-Interstate NHS within the MPO boundary
Peak Hour Travel Time Ratio | Interstates within the Urbanized Area Boundary > 1 million Non-Interstate NHS within the Urbanized Area Boundary > 1 million
Truck Travel Time Reliability | Interstates within the MPO boundary
Average Truck Speed | 

## Slide 34: Thank You

## Slide 35: Questions?